Architectural Components Group, Inc.

521 George St.

Marshfield, MO 65706

417-869-6777  /  417-869-7888 fax

info@acgiwood.com / acgiwood.com

ARCHITECTURAL SPECIFICATIONS

FOR LINEAR CLOSED SERIES 1

WOOD WALL & CEILING SYSTEM

[Project Name]

[Project Location]

PART 1 — GENERAL

1.1 Description of Work:

- Work Included: Provide Architectural Components Group, Inc. Linear Closed Series 1 LC1 wood wall and ceiling system where shown on architectural drawings, and as specified in this specification.

1.2 Quality Assurance:

- Architectural Components Group, Inc. LC1-xxxx-C Linear Closed wood wall and ceiling system for this project shall maintain the quality as instituted by the architect or A.W.I.

- Design Criteria: Manufacture of Linear Closed wood wall and ceiling system LC1-xxxx-C shall be installed true and plumb to within manufacturing tolerance of 1/8” within 8’ of length.

- Product Construction: Wood shall be kiln dried to 10%. Cracking, checking and warpage of members will not be acceptable.

1.3 Submittals:

- Technical Data: Submit manufacturer’s data and installation instructions.

- Shop Drawings: Submit 4 copies of shop drawings showing all areas involved, attachment conditions and perimeter circumstances.

- Submittal Sample: Submit 1 product sample for approval by architect.

1.4 DELIVERY, STORAGE AND HANDLING

- Material must be stored and installed only in secured ambient environment (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- Windows, doors and all wet-work must be completed before unpacking and installation. Handle carefully to avoid damage.

PART 2 — PRODUCTS

2.1 Acceptable Manufacturer:

Architectural Components Group, Inc. 521 George St., Marshfield, MO 65706

Phone (417) 869-6777	Fax (417) 869-7888

2.2 Product Type

- Product Configuration: Linear Closed Series 1 wood system product: LC1-xxxx-C

Nomenclature for LC1-325-C:

LC1 = Linear Closed Series 1

325 = 3-1/4” wide

C = 3/4” thick plank

- Wood planks shall be provided in a size of: x” wide x 3/4” thick.

- Wood plank length shall be random length up to 10’ length (if solid wood) or 8’ and/or 10’ length (if veneer).

- Wood Specie: System shall consist of desired solid wood or veneer; wood specie.

- Finish: Wood finish shall utilize ACGI clear finish with satin sheen or specify stain to match architect sample. Back of planks shall be factory sealed.

- Certification: If solid wood, wood shall or shall not be FSC certified. If wood veneer, wood veneer shall or shall not be FSC certified, and the core material shall or shall not be FSC certified. If FSC, Chain of Custody shall or shall not be provided.

- NAUF: If veneer, substrate material shall or shall not be manufactured with no added urea formaldehyde.

- Fire Rating: Panels shall achieve a Class I(A) or Class III(C) Fire Rating.

- Attachment System: Linear Wood Wall and Ceiling System shall be suspended according to manufacturer’s suggested method of suspension as per the design details provided in the plans.

PART 3 — EXECUTION

3.1 Installation

- Linear wood wall and ceiling system shall be handled and installed with care in order to prevent surface and structure damage. Field cutting shall be kept to a minimum and performed as recommended by manufacturer.

- The contractor shall suspend panels in accordance with manufacturer’s recommended installation guides and shop drawings

- The ceiling system shall be suspended by 15/16” black HD T-grid with main runners on 2’ centers and cross T’s every 4’.

- Panels shall be installed by screwing LSC-101 and LSC-102 clips into the furring strips (wall) or T-Grid (ceiling) and attaching the wood members in accordance to the manufactures’ installation instructions.  LSC-103 alignment clips shall be used at plank joints.

- Contractor shall clean all panels prior to installation according to manufacturer’s recommended maintenance procedures. Upon completion of installation, panels shall be inspected and cleaned as needed.

PART — 4 WARRANTY

4.1 Product Warranty

- Architectural Components Group, Inc. shall warranty the Linear wood wall and ceiling system against manufacturer’s defects up to one year. Changes in finish or dimensions due to ultra violet light, excessive temperature or humidity conditions and/or abuse of any kind shall void any warranties from ACGI.

- Install conditions for the area should remain for the proper occupied conditions of humidity and temperature (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- The contractor shall warranty for one year all work from final acceptance of completed work.