ARCHITECTURAL SPECIFICATIONS FOR

WOOD MICRO GRILLE SERIES 1

CEILING OR WALL SYSTEM

[Project Name]

[Project Location]

PART 1 — GENERAL

1.1 Description of Work

- Work Included: Provide Architectural Components Group, Inc. Micro Grille ceiling or wall system where shown on architectural drawings, and as specified in this specification.

1.2 Quality Assurance

- Architectural Components Group, Inc. MG1-xxxx-yyy-C wood Micro Grille ceiling or wall System for this project shall maintain the quality as instituted by the architect or A.W.I.

- Design Criteria: Manufacture of MG1-xxxx-yyy-C wood Micro Grille shall be installed true and plumb to within manufacturing tolerance of 1/8” within 8’ of length.

- Product Construction: Wood shall be kiln dried to 10%. Cracking, checking and warpage of members will not be acceptable.

1.3 Submittals

- Technical Data: Submit manufacturer’s data and installation instructions.

- Shop Drawings: Submit 4 copies of shop drawings showing all areas involved, attachment conditions and perimeter circumstances.

- Submittal Sample: Submit 1 product sample for approval by architect.

1.4 Delivery, Storage and Handling

- Material must be stored and installed only in secured ambient environment (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- Windows, doors and all wet-work must be completed before unpacking and installation. Handle carefully to avoid damage.

PART 2 — PRODUCTS

2.1 Acceptable Manufacturer

Architectural Components Group, Inc., 521 George Street, Marshfield, MO 65706 Phone (417) 869-6777	Fax (417) 869-7888

2.2 Product Type

- Product Configuration: Wood Micro Grille system product: MG1-xxxx-yyy-C

Nomenclature for: MG1-24100-.25

MG1 = Micro Grille series 1

24 = 24 blades per foot

100 = 1” blade depth

.25 = 1/4” thickness of blade

- Wood Micro Grille members shall be provided in panel maximum width of 2’ and maximum panel length of nominal 10’ [9’ 11”] in 1’ increments.

- Factory assembled with black backers at 12” on center.

- Finish: Wood finish shall utilize ACGI clear finish with satin sheen or specify custom stain to match architect sample.

- Wood specie shall be specie solid wood.

- Certification: Solid wood shall or shall not be FSC certified. If FSC, Chain of Custody shall or shall not be provided.

- Fire Rating: Micro Grilles shall achieve a Class I(A) or Class III(C) fire rating.

- Attachment System: Wood Micro Grille ceiling or wall system shall be suspended according to manufacturers suggested method of suspension as per the design details provided in the plans.

PART 3 — EXECUTION

3.1 Installation

- Wood Micro Grille ceiling or wall system shall be handled and installed with care in order to prevent surface and structure damage. Field cutting shall be kept to a minimum and performed as recommended by manufacturer.

- The ceiling system shall be suspended by HD T-grid with main runners on 2’ centers and cross T’s every 4’.

PART 4 — WARRANTY

4.1 Product Warranty

- Architectural Components Group, Inc. shall warranty the wood Micro Grille ceiling or wall system against manufacturer’s defects up to one year. Changes in finish or dimensions due to ultra violet light, excessive temperature or humidity conditions and/or abuse of any kind shall void any warranties from ACGI.

- Install conditions for the area should remain for the proper occupied conditions of humidity and temperature (humidity min. 25% - max. 55%, temperature not to exceed 86 degrees).

- The contractor shall warranty for one year all work from final acceptance of completed work.

# Text boxes

Architectural Components Group, Inc.

521 George St.

Marshfield, MO 65706

417-869-6777  /  417-869-7888 fax

info@acgiwood.com / acgiwood.com