Armstrong World Industries, Inc.

Please understand that you are responsible for the accuracy of all project specifications, including any Armstrong guide specifications that you use.

ARMSTRONG SHALL NOT BE LIABLE FOR ANY DAMAGES ARISING OUT OF THE USE OF ANY OF ITS GUIDE SPECIFICATIONS.

SECTION 09 77 14

WOOD VENEER WALL PANELS

PART 1 - GENERAL

1.1  	RELATED DOCUMENTS

Drawings and general conditions of Contract, including General and Supplementary Conditions and Divisions-1 Specification sections apply to work of this section.

1.2	SUMMARY

A.	Section Includes:

1.	Acoustical wall panels and installation components.

B.	Related Sections:

- Section 09 20 00 (09200) – Plaster and Gypsum Board

- Division 26 (16) Sections - Electrical Work

C. 	Alternates

1.   Prior Approval: Unless otherwise provided for in the Contract documents, 	proposed product substitutions may be submitted no later than TEN (10) working days prior to the date established for receipt of bids.  Acceptability of a proposed 	substitution is contingent upon the Architect’s review of the proposal for 	acceptability and approved products will be set forth by the Addenda.  If included in a Bid are substitute products which have not been approved by Addenda, the specified products shall be provided without additional compensation.

2.   Submittals which do not provide adequate data for the product evaluation will not 	be considered.  The proposed substitution must meet all requirements of this 	section, including but not necessarily limited to, the following: Single source 	materials suppliers (if specified in Section 1.5); Panel design, size, composition, color, and finish; installation system component profiles and sizes; Compliance with the referenced standards.

1.3	REFERENCES

A.	Test Methods:

- ASTM C 423 Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method.

- ASTM E 84/CAN/ULC S102 Standard Test Method for Surface Burning Characteristics of Building Materials.

- CAN/ULC S102 Standard Test Method for Surface Burning Characteristics of Building Materials.

1.4	SUBMITTALS

A.	Product Data:  Submit manufacturer’s technical data for each type of acoustical wall panel required.

B.	Samples:  Minimum 3 inch x 3 inch samples of specified acoustical wall substrate; minimum 4 inch long samples of attachment method including trim and decorative accents.

- Shop Drawings:  Submit shop drawings showing how panels are to be laid out on the walls, details of trim members and width of panels.  Width of panels and location of vertical seams are critical.

1.5	QUALITY ASSURANCE

- Single-Source Responsibility:  Provide acoustical panel units and installation components by a single manufacturer.

- Fire Performance Characteristics:  Identify acoustical wall components with appropriate markings of applicable testing and inspecting organization.

1.	Surface Burning Characteristics:  As follows, tested per ASTM E 84,

a.	Flame Spread:  25 or less

- Smoke Developed:  50 or less

C.	Coordination of Work:  Coordinate acoustical wall work with installers of related work including, but not limited to building insulation, gypsum board, light fixtures, mechanical systems, electrical systems, and sprinklers.

1.6	DELIVERY, STORAGE, AND HANDLING

A.	Deliver acoustical wall panels to project site in original, unopened packages and store them in a fully enclosed space where they will be protected against damage from moisture, direct sunlight, surface contamination, and other causes.

B.	Before installing acoustical wall panels, permit them to reach room temperature and a stabilized moisture content.

C.	Handle acoustical wall panels carefully to avoid chipping edges or damaged units in any way.

1.7	PROJECT CONDITIONS

A.	Space Enclosure:

Wood veneer wall panel materials should be permitted to reach room temperature and have a stabilized moisture content for a minimum of 72 hours before installation.

The wood veneer panels should not be stored or installed in spaces where the temperature or humidity conditions vary greatly from the temperatures and conditions that will be normal in the occupied space.

As interior finish products, the wood veneer panels are designed for installation in temperature conditions between 50 degrees F and 86 degrees F, in spaces where the building is enclosed and HVAC systems are functioning and will be in continuous operation.  Relative humidity should not fall below 25 percent or exceed 55 percent.

1.8	WARRANTY

A.	Wall Panel:  Submit a written warranty executed by the manufacturer, agreeing to repair or replace acoustical panels that fail within the warranty period.  Failures include, but are not limited to:

1.	Wall Panels:  Manufacturer’s defects

B.	Warranty Period:

- Wall panels:  One (1) year from date of substantial completion.

C.   The Warranty shall not deprive the Owner of other rights the Owner may have under other provisions of the Contract Documents and will be in addition to and run concurrent with other warranties made by the Contractor under the requirements of the Contract Documents.

1.9	MAINTENANCE

A.	Extra Materials:  Deliver extra materials to Owner.  Furnish extra materials described below that match products installed.  Packaged with protective covering for storage and identified with appropriate labels.

1.	 Wall Panels:  Furnish quantity of full-size units equal to 5.0 percent of amount installed.

PART 2 - PRODUCTS

2.1	MANUFACTURERS

A.	Acoustical Wall Panels:

1.	Armstrong World Industries, Inc.

2.2	ACOUSTICAL WALL PANELS

A.	 Wall Panels: Type AWP-1:

- Surface Texture:  Smooth

- Composition:  Particle Board

- Finish: Natural Variations(Beech)(Maple)(Light Cherry)(Dark Cherry)(Oak)(Walnut)(Walnut Espresso), Bamboo (Patina)(Native)

- Size: (24 inches X 48 inches X 3/4 inch)(24 inches X 96 inches X 3/4 inch)(24 inches X 108 inches X 3/4 inch)(24 inches X 120 inches X 3/4 inch)

- Edge Profile: K2C2 both vertical edges for interface

- Noise Reduction Coefficient (NRC):  ASTM C 423;

a. W2 Perforation: 0.50 (D Mounting with Acoustical Fleece), 0.65 (DMounting with 1 inch Fiberglass Backer)

b. W3 Perforation: 0.50 (D Mounting with Acoustical Fleece), 0.65 (D Mounting with 1 inch Fiberglass Backer)

c. W4 Perforation: 0.55 (D Mounting with Acoustical Fleece), 0.80 (D Mounting with 1 inch Fiberglass Backer)

d. W5 Perforation: 0.45 (D Mounting with Acoustical Fleece), 0.70 (D Mounting with 1 inch Fiberglass Backer)

e. W6 Perforation: 0.45 (D Mounting with Acoustical Fleece, 0.60 (D Mounting with 1 inch Fiberglass Backer)

- Flame Spread:  ASTM E84 (HPVA), Class A

- Dimensional Stability:  Standard – space must be enclosed with HVAC systems operating at all times.

- Acceptable Product:  Woodworks Walls, item #______, as manufactured by Armstrong World Industries.

B.	 Wall Panel Accessories:

1. Decorative Accent Trims and Splines

a. Wall Installation Spline (concealed): Item #5858__BLY, 8 foot, 9 foot or 10 foot, Black Aluminum

2. Moldings:

a. 4 inch Base Molding: Item #5855____, 8 feet 4 inches, Solid Wood

b. 6 inch Base Molding: Item #5856____, 8 feet 4 inches, Solid Wood                                        c. 1.15 inch Finish Molding: Item #5857____, (8 feet 4 inches)(9 feet 4inches)(10 feet 2      inches), Solid Wood

C. Decorative Corners and Splines:

a. Peak Corner: Item #5851____, (8feet)(9 feet)(9 feet 10 inches), Solid Wood

b. Bullnose Corner, Item #5852____, (8 feet)(9 feet)(9 feet 10 inches), Solid Wood

c. Corner Installation Spline (concealed), 5859____, (8 feet)(9 feet)(9 feet 10 inches),   Plastic or Aluminum

D. Chair Rail Accessories:

a. Mounting Rail: Item #5861___, 8 feet 4 inches, Solid Wood

b. Rail Insert: Item #5863___, 8 feet 4 inches, Solid Wood

c. Rail Insert-Aluminum: Item #5963NA, 8 feet, Solid Wood and Aluminum

d. Rail Cap: Item #5864___, 8 feet 4 inches, Solid Wood

e. Easel Ledge, Item #5866___, 8 feet 4inches, Solid Wood

PART 3 - EXECUTION

3.1	EXAMINATION

A.	Do not proceed with installation until all wet work such as concrete, terrazzo, plastering and painting has been completed and thoroughly dried out, unless expressly permitted by manufacturer’s printed recommendations.

3.2	PREPARATION

A.	Measure each wall area and establish layout of acoustical units to balance border widths at opposite edges of each wall.  Coordinate panel layout with mechanical and electrical fixtures.

3.3	INSTALLATION

- Install wall panels by attaching the panels to an existing wall per the manufacturer’s instructions, LA 297712, and in accordance with the authorities having jurisdiction.

3.4	ADJUSTING AND CLEANING

A.	Replace damaged and broken panels.

B.	Use a clean, dry, soft, white cloth to wipe off any dirt or greasy fingerprints. If this does not clean the panel, use a damp clean soft white cloth or sponge with a mild detergent to wipe the panel.

END OF SECTION